## Slide 1: CSCI U511 01 Operating Systems AKM Jahangir A Majumder, PhD
Fall 2019 - Lecture 2
August 27, 2019
Note: Some slides are adapted from those used by previous instructors and some slides include figures from the textbook.

## Slide 2: Review and Learning Outcomes
We will finish to discuss introduction to OS systems (Chap. 1) today
We will review materials covered in CSCI U 210 and 310 today
Please read the syllabus
We will have our first quiz on Thursday, September 5 which will cover lectures 1-3
HW 1 will post on Blackboard soon which is due on Tuesday, Sept. 3
The project proposal is due today.

## Slide 3: Review: Today’s Operating Systems- Computers Cheap
Smartphones
Embedded systems
Laptops
Tablets
Virtual machines
Data center servers

## Slide 4: Review: Tomorrow’s Operating Systems
Giant-scale data centers
Increasing numbers of processors per computer
Increasing numbers of computers per user
Very large scale storage

## Slide 5: The major OS issues
structure: how is the OS organized?
sharing: how are resources shared across users?
naming: how are resources named (by users or programs)?
security: how is the integrity of the OS and its resources ensured?
protection: how is one user/program protected from another?
performance: how do we make it all go fast?
reliability: what happens if something goes wrong (either with hardware or with a program)?
extensibility: can we add new features?
communication: how do programs exchange information, including across a network?

## Slide 6: Major issues in OS (2)
Concurrency: how are parallel activities created and controlled?
Scale and growth: what happens as demands or resources increase?
Persistence: how to make data last longer than programs
Compatibility & Legacy Apps: can we ever do anything new?
Distribution: Accessing the world of information
Accounting: who pays the bills, and how do we control resource usage?
These are engineering trade-offs
Based on objectives and constraints

## Slide 7: Progression of concepts and form factors
© Silberschatz, Galvin and Gagne

## Slide 8: Has it all been discovered?
New challenges constantly arise
  embedded computing (e.g., iPod)
  sensor networks (very low power, memory, etc.)
  peer-to-peer systems
  ad hoc networking
  scalable server farm design and management (e.g., Google)
  software for utilizing huge clusters (e.g., MapReduce, Bigtable)
  overlay networks (e.g., PlanetLab)
  worm fingerprinting
  finding bugs in system code (e.g., model checking)
Old problems constantly re-define themselves
  the evolution of PCs recapitulated the evolution of minicomputers, which had recapitulated the evolution of mainframes
  but the ubiquity of PCs re-defined the issues in protection and security

## Slide 9
An illustration of architectural and OS functionality requirements
OS
User program

## Slide 10: Parallel systems
Some applications can be written as multiple parallel threads or processes
  can speed up the execution by running multiple threads/processes simultaneously on multiple CPUs
  need OS and language primitives for dividing program into multiple parallel activities
  need OS primitives for fast communication among activities
    degree of speedup dictated by communication/computation ratio
  many flavors of parallel computers today
    SMPs (symmetric multi-processors, multi-core)
    MPPs (massively parallel processors)
    NOWs (networks of workstations)
    computational grid (SETI @home)

## Slide 11: Personal computing
Primary goal was to enable new kinds of applications
Bit mapped display
  new classes of applications
  new input device (the mouse)
Move computing near the display
  why?
Window systems
  the display as a managed resource
Local area networks [Ethernet]
  why?
Effect on OS?

## Slide 12: Client/server computing
Mail server/service
File server/service
Print server/service
Compute server/service
Game server/service
Music server/service
Web server/service
etc.

## Slide 13: Embedded/mobile/pervasive computing
Pervasive computing
  cheap processors embedded everywhere
  how many are on your body now? in your car?
  cell phones, PDAs, network computers, …
Typically very constrained hardware resources
  slow processors
  very small amount of memory (e.g., 8 MB)
  no disk
  typically only one dedicated application
  limited power
But this is changing rapidly!

## Slide 14: In Lecture Review
We finished our coverage on Chapter 1
We will begin our coverage on Chap 2: Kernels and Processes
But we will review U210 course syllabi before we start to discuss Chap 2

## Slide 15: Review on U210

## Slide 16: Performance: CPU Time
Performance improved by
  Reducing number of clock cycles
  Increasing clock rate
  Hardware designer must often trade off clock rate against cycle count

## Slide 17: Performance Summary
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 18: Different Logic Gates
A
B
AB
A
B
A+B
A
A’
A
B
(A.B)’
A
B
(A+B)’
(A+B)
A
B
AND
OR
NOT
NAND
NOR
XOR
You need to memorize their symbols and functions

## Slide 19: Boolean Algebra and Truth Table
Boolean algebra can be used to describe binary logic.
Boolean algebra operators (in the order of priority):
  () : Parenthesis
  ‘ : NOT
   : AND
  + : OR
Truth table can be used to represent input-output relations of a digital system.
You should be able to derive a truth table for a given logic circuit or Boolean algebra presentation and vice versa.

## Slide 20: Example: Truth Table, Boolean Algebra, and Digital Logic Circuit
A | B | C | BC | A+BC
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
C
B
BC
A
A+BC

## Slide 21: Constructing Gates
It turns out that, because the way a transistor works, the easiest gates to create are the NOT, NAND, and NOR gates

## Slide 22: Laws of Boolean Algebra
Identity law
  A + 0 = A
  A1 = A
Zero and One laws
  A + 1 = 1
  A 0 = 0
Inverse laws
  A + A’ = 1
  A A’ = 0
Commutative laws
  A + B = B + A
  A . B = B . A
Associative laws
  A + (B + C) = (A + B) + C
  A . (B . C) = A . (B . C)
Distributive laws
  A. (B + C) = (A.B) + (B.C)
  A+(B . C) = (A+B) . (A+C)
DeMorgan’s laws
  (AB)’=A’+B’
  (A+B)’=A’ B’

## Slide 23: Binary Numbers
Some terminology and units
  Bit (b): A single binary digit
  Nib: 4 bits
  Byte (B): 8-bits
  Word: A group of bits of any size (often 4 bytes).
  kb: 210 bits = 1024 bits (kB = 210 bytes)
  Mb: 220 bits =1,048,576 bits (MB = 220 bytes)
  Gb: 230 bits = 1,073,741,820 bits (GB = 230 bytes)
  MSB: Most significant bit (leftmost digit of binary #)
  LSB: Least significant bit (rightmost digit of bin. #)

## Slide 24: Binary to Decimal Conversion
···b3b2b1b0 (each bit bi is 0 or 1)
b0×20 + b1×21 + b2×22 + b3×23 + ···
= b0×1 + b1×2 + b2×4 + b3×8 + ···
Binary Number:
Its decimal value is:
Examples: 11102 Decimal value is:
11112 Decimal value is:
1100102 Decimal value is:
1111112 Decimal value is:
Check your understanding:
N bits  2N combinations  decimal numbers 0, 1, 2, 3, …, 2N - 1
The largest number: 11…112 = 2N-1 (decimal)
14
15
50
63
N bits, all ones

## Slide 25: Other Conversions
Convert decimal to hex
Use the successive division method described previously (for decimal to binary), but divide by 16 instead of 2.
Convert binary to hex
  A hex digit is equivalent to 4 bits.
  Divide binary number into groups of 4 bits, starting from the right.
  Convert each 4 bit group into one hex digit.
Convert hex to binary
  Convert each hex digit to its 4-bit binary equivalent.
  String the bits together.
Note: Computationally, it’s easy to convert between bases that are powers of 2, as indicated in the binary to hex conversion technique above.

## Slide 26: Other Conversions
Convert decimal to Octal
Use the successive division method described previously (for decimal to binary), but divide by 8 instead of 2.
Convert binary to Octal
  A octal digit is equivalent to 3 bits.
  Divide binary number into groups of 3 bits, starting from the right.
  Convert each 3 bit group into one octal digit.
Convert octal to binary
  Convert each octal digit to its 3-bit binary equivalent.
  String the bits together.
(examples on next slide)

## Slide 27: Fractions
Binary number: 0.b-1b-2b-3b-4···
Decimal value: b-1×2-1 + b-2×2-2 + b-3×2-3 + b-4×2-4 + ···
Binary to Decimal Conversion
Decimal to Binary Conversion: Successive multiplication by 2
Example: Decimal number 0.6875
Example: 0.1012 = 1×2-1 + 0×2-2 + 1×2-3 = 0.62510
0.68752 = 1.375  b-1 = 1 and 1.375-1 = 0.375
0.3752 = 0.75  b-2 = 0 and 0.75-0 = 0.75
0.752 = 1.5  b-3=1 and 1.5-1 = 0.5
0.52 = 1  b-4=1 and 1-1 = 0
Binary representation: 0.1011

## Slide 28: 1 Bit Full Adder Implementation
cin
b
a
s
Å
Å
=
cin
)
b
a
(
b
a
cout
Å
+
=
a
b
carry in
carry out
sum

## Slide 29: Binary Math: 2’s Complement
In binary world, people use 2’s complement to represent signed integer and implement subtraction.
The procedure of getting 2’s complement of a given number:
  Invert every bit
  Then add 1
For n bit signed integer, its representation is -2n-1 ~ 2n-1-1
  Example
    110011002 = - (00110100)2 = -5210
    100000002 = -12810

## Slide 30: 2’s Complement Adder/Subtractor
Subtraction can be done by addition of the 2's Complement.
1. Complement each bit
2. Add 1 to the result.
The circuit shown computes A + B and A – B:
For S = 1, subtract, the 2’s complement of B is formed by using XORs to form the 1’s comp and adding the 1 applied to C0.
For S = 0, add, B is passed through unchanged

## Slide 31: Binary Math: Overflow Detection
Overflow happens when the calculation result is beyond the representation range for given number of bits.
Overflow might happen in one of following situations:
  Positive + Positive
  Negative + Negative
  Positive – Negative
  Negative – Positive
Important: You should determine whether an overflow happen by checking sign bits.
Example:
  Overflow: 11000000+10000000=01000000 (the extra carry out bit is discarded)
  Overflow: 01000000+01000000=10000000 (no extra bit)
  No Overflow 01000000+11000000=00000000 (the extra carry out bit is discarded)

## Slide 32: Multiplication and Division by Shifting Bits
We will cover multiplication in great details later. However, some simple multiplication can be accomplished simply by shifting the bit sequence.

## Slide 33: Shift Operations
Move (shift) all the bits in a word to the left or right by a number of bits.
  Example: shift right by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0000 0000 0001 0010 0011 0100 0101 0110
  Example: shift left by 8 bits
  0001 0010 0011 0100 0101 0110 0111 1000
  0011 0100 0101 0110 0111 1000 0000 0000

## Slide 34: Shifting and Multiplication
Shift Left a binary number by i bits will give the same result as multiplying by 2i. (True or False)
Shift Right a binary number by i bits will give the same result as dividing by 2i. (True or False)

## Slide 35: Decoder
Popular combinational logic building block, in addition to logic gates
Collection of logic gates which are arranged in a specific way that converts input binary number to one high output
2-input decoder: four possible input binary numbers... So has four outputs, one for each possible input binary number

## Slide 36: Building of 4-to-1-line Multiplexer
2-to-22-line decoder
22 ´ 2 AND-OR

## Slide 37: The ALU Diagram
ALU control lines: 0000 = and 0001 = or 0010 = add 0110 = subtract 0111 = slt 1100 = NOR
ALU 0~30
ALU 31
Can this ALU implement a NAND function?

## Slide 38: Introduction to Sequential Circuits
A Sequential circuit contains:
  Storage elements: Latches or Flip-Flops
  Combinatorial Logic:
    Implements a multiple-output switching function
    Inputs are signals from the outside.
    Outputs are signals to the outside.
    Other inputs, State or Present State, are signals from storage elements.
    The remaining outputs, Next State are inputs to storage elements.
Combina-tional
Logic
Storage Elements
Inputs
Outputs
State
Next
State

## Slide 39: Storage Element’s Timing Model
Setup Time: Input must be stable BEFORE trigger clock edge
Hold Time: Input must REMAIN stable after trigger clock edge
Clock-to-Q time:
  Output cannot change instantaneously at the trigger clock edge
  Similar to delay in logic gates, two components:
    Internal Clock-to-Q
    Load dependent Clock-to-Q
Typical for class: 1ns Setup, 0.5ns Hold
D
Q
D
Don’t Care
Don’t Care
Clk
Unknown
Q
Setup
Hold
Clock-to-Q
Notes: So far we have been looking at combinational logic, let’s look at the timing characteristic of a storage element.
The storage element you will use is a D type flip-flop trigger on the negative clock edge.
In order for the data to latch into the flip flop correctly, the input must be stable slightly before the falling edge of the clock. This time is called the Setup time.
After the clock edge has arrived, the data must remain stable for a short amount of time AFTER the trigger clock edge. This is called the hold time.
The output cannot change instantaneously at the trigger clock edge. The time it takes for the output to change to its new value after the clock is called the Clock-to-Q time.
Similar to delay in logic gates, the Clock-to-Q time has two components:
(a) The internal Clock-to-Q time: the time it takes the output to change if output load is zero.
(b) And the load dependent Clock-to-Q time.
+2 = 50 min. (Y:30)

## Slide 40: Machine Format
Our processor’s machine code format is given below
  [load, regad1, regad2, des_regad, aluop]
    load signal: 1 (read from external input), 0 (read from ALU)
    regad1: the address of the register for the ALU input 1
    regad2: the address of the register for the ALU input 2
    des_regad: the address of the destination register which data is written into
    aluop: the ALU function selection
There are 16 registers and 8 ALU functions.
Question: Based on the above description of the processor, how many bits each command should have?

## Slide 41: MIPS Assembly Language
We’ll be working with the MIPS instruction set architecture
  developed in 1985
  means “Microprocessor without Interlocked Pipeline Stages”
  similar to other architectures developed since the 1980's
  almost 100 million MIPS processors manufactured in 2002
  used by NEC, Nintendo, Cisco, Silicon Graphics, Sony, …
  a Reduced Instruction Set Computer (RISC) Assembly Language
Instruction Category:
  Arithmetic: Add, Subtract,…
  Data Transfer: Load Word,…
  Logical: And, Or,…
  Conditional Branch: Branch on Equal,…
  Unconditional Jump: Jump

## Slide 42: Assembly Variables: Registers Cont..
Registers are numbered from 0 to 31
Each register can be referred to by number or name
Number references:
  $0, $1, $2, … $30, $31

## Slide 43: MIPS Registers
USE Number Name
The constant 0 $0 $zero
Reserved for Assembler $1 $at
Return Values $2-$3 $v0-$v1
Arguments $4-$7 $a0-$a3
Temporary $8-$15 $t0-$t7
Saved Temporaries $16-$23 $s0-$s7
Temporary $24-$25 $t8-$t9
Used by Kernel $26-$27 $k0-$k1
Global Pointer $28 $gp
Stack Pointer $29 $sp
Frame Pointer $30 $fp
Return Address $31 $ra

## Slide 44: Registers vs. Memory
Arithmetic instructions operands must be registers, — only 32 registers provided
Which computer components do registers belongs to?
Compiler associates variables with registers
What about programs with lots of variables?
Processor
I/O
Control
Datapath
Memory
Input
Output

## Slide 45: Review: MIPS Instruction Format
OP
OP
OP
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide

## Slide 46: Machine Language: R-Type
Numeric version of instructions is called machine language
Instructions, like registers and words of data, are also 32 bits long
  Example: add $t0, $s1, $s2
  registers have numbers, $t0=8, $s1=17, $s2=18
Instruction Format: add $t0, $s1, $s2
000000 10001 10010 01000 00000 100000 op rs rt rd shamt funct
Can you guess what the field names stand for?
Notes: Board work: Binary Numbers

## Slide 47: Machine Language: I-Type
Consider the addi instructions,
  What would the regularity principle have us do?
  New principle: Good design demands a compromise
Introduce a new type of instruction format
  I-type for immediates
  other format was R-type for register
Example: addi $s1, $s2, 100 8 18 17 100 op rs rt 16 bit number

## Slide 48: MIPS Fields
op: Basic operation of the instruction, opcode
rs: The first register source operand
rt: The second register source operand
rd: The register destination operand.
shamt: Shift amount
funct: Function

## Slide 49: Assembly Operands: Memory
C variables map onto registers; what about large data structures like arrays?
1 of 5 components of a computer: memory contains such data structures
But MIPS arithmetic instructions only operate on registers, never directly on memory.
Data transfer instructions transfer data between registers and memory:
  Memory to register
  Register to memory

## Slide 50: Anatomy: 5 components of any Computer
Personal Computer
Processor
Computer
Control
(“brain”)
Datapath
Registers
Memory
Devices
Input
Output
Load (from)
Store (to)
These are “data transfer” instructions…
Registers are in the datapath of the processor; if operands are in memory, we must transfer them to the processor to operate on them, and then transfer back to memory when done.
Notes: That is, any computer, no matter how primitive or advance, can be divided into five parts:
1. The input devices bring the data from the outside world into the computer.
2. These data are kept in the computer’s memory until ...
3. The datapath request and process them.
4. The operation of the datapath is controlled by the computer’s controller.
All the work done by the computer will NOT do us any good unless we can get the data back to the outside world.
5. Getting the data back to the outside world is the job of the output devices.
The most COMMON way to connect these 5 components together is to use a network of busses.

## Slide 51: Data Transfer: Memory to Reg (1/4)
To transfer a word of data, we need to specify two things:
  Register: specify this by # ($0 - $31) or symbolic name ($s0,…, $t0, …)
  Memory address: more difficult
    Think of memory as a single one-dimensional array, so we can address it simply by supplying a pointer to a memory address.
    Other times, we want to be able to offset from this pointer.
Remember: “Load FROM memory”

## Slide 52: Data Transfer: Memory to Reg (3/4)
Load Instruction Syntax:
  1 2, 3(4)
  where
  1) operation name
  2) register that will receive value
  3) numerical offset in bytes
  4) register containing pointer to memory
MIPS Instruction Name:
  lw (meaning Load Word, so 32 bits or one word are loaded at a time)

## Slide 53: Data Transfer: Memory to Reg (4/4)
Example: lw $t0,12($s0)
  This instruction will take the pointer in $s0, add 12 bytes to it, and then load the value from the memory pointed to by this calculated sum into register $t0
Notes:
  $s0 is called the base register
  12 is called the offset
  offset is generally used in accessing elements of array or structure: base reg points to beginning of array or structure
Data flow

## Slide 54: Data Transfer: Reg to Memory
Also want to store from register into memory
  Store instruction syntax is identical to Load’s
MIPS Instruction Name:
sw (meaning Store Word, so 32 bits or one word are loaded at a time)
Example: sw $t0,12($s0)
  This instruction will take the pointer in $s0, add 12 bytes to it, and then store the value from register $t0 into that memory address
Remember: “Store INTO memory”
Data flow

## Slide 55: The First Program: Hello World
.text
.globl main
main:
li $v0, 4
la $a0, str
syscall # print string
li $v0, 10
syscall # exit (you must use syscall #10 to exit)
.data
str: .asciiz "Hello World!!!"

## Slide 56: MIPS Data Transfer Instructions Example
C code: A[12] = h + A[8]; MIPS code: lw $t0, 32($s3) # load word add $t0, $s2, $t0 sw $t0, 48($s3) # store word
$s3: base address (as called index register)
Can refer to registers by name (e.g., $s2, $t2) instead of number
Store word has destination last
Remember arithmetic operands are registers, not memory! Can’t write: add 48($s3), $s2, 32($s3)
Word Address
Byte Address

## Slide 57: More Notes about Memory: Alignment
MIPS requires that all words start at byte addresses that are multiples of 4 bytes
0 1 2 3
Aligned
Not
Aligned
Called Alignment: objects must fall on address that is multiple of their size.
0, 4, 8, or Chex
Last hex digit of address is:
1, 5, 9, or Dhex
2, 6, A, or Ehex
3, 7, B, or Fhex

## Slide 58: MIPS Control Instruction I: Conditional Branch
Decision making instructions
  alter the control flow,
  i.e., change the "next" instruction to be executed
MIPS conditional branch instructions:
bne $t0, $t1, Label : if ($t0!=$t1) go to Label beq $t0, $t1, Label : if ($t0==$t1) go to Label
Example: if (i==j) h = i + j; bne $s0, $s1, Label add $s3, $s0, $s1 Label: ....

## Slide 59: MIPS Control Instruction II: Unconditional Jump
MIPS unconditional branch instructions: j label
Example: if (i!=j) beq $s4, $s5, Lab1 h=i+j; add $s3, $s4, $s5 else j Lab2 h=i-j; Lab1: sub $s3, $s4, $s5 Lab2: ...
Technically, it’s the same as:
  beq $0,$0,label
  since it always satisfies the condition.

## Slide 60: Example: Compiling C if into MIPS (1/2)
Compile by hand
  if (i == j) f=g+h; else f=g-h;
Use this mapping: f: $s0 g: $s1 h: $s2 i: $s3 j: $s4
Exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j

## Slide 61: Example: Compiling C if into MIPS (2/2)
Final compiled MIPS code:
beq $s3,$s4,True # branch i==j sub $s0,$s1,$s2 # f=g-h(false) j Fin # goto Fin True: add $s0,$s1,$s2 # f=g+h (true) Fin:
Note: Compiler automatically creates labels to handle decisions (branches). Generally not found in HLL code.
Exit
i == j?
f=g+h
f=g-h
(false) i != j
(true) i == j
Compile by hand
  if (i == j) f=g+h; else f=g-h;

## Slide 62: Inequalities in MIPS (1/5)
Until now, we’ve only tested equalities (== and != in C). General programs need to test < and > as well.
Create a MIPS Inequality Instruction:
  “Set on Less Than”
  Syntax: slt reg1,reg2,reg3
  Meaning: reg1 = (reg2 < reg3);
  if (reg2 < reg3) reg1 = 1; else reg1 = 0;
  Usually, “set” means “set to 1”, “reset” means “set to 0”.
Same thing…

## Slide 63: Inequalities in MIPS (2/5)
How do we use this? Compile by hand: if (g < h) goto Less; #g:$s0, h:$s1
Answer: compiled MIPS code…
slt $t0,$s0,$s1 # $t0 = 1 if g<h bne $t0,$0,Less # goto Less # if $t0!=0 # (if (g<h)) Less:
Branch if $t0 != 0  (g < h)
Register $0 always contains the value 0, so bne and beq often use it for comparison after an slt instruction.
A slt  bne pair means if(… < …)goto…

## Slide 64: Inequalities in MIPS (3/5)
We covered two pseudo instructions, li and la, in our SPIM tutorial session.
The following pseudo instruction is also useful:
"blt $s1, $s2, Label“
    called “branch on less than”
    can now build general control structures
Note that the assembler needs a register ($at: assembler temporary) to do this,
  there are policy of use conventions for registers
Notes: Board work: Binary Numbers

## Slide 65: Inequalities in MIPS (4/5)
Now, we can implement <, but how do we implement >, ≤ and ≥ ?
We could add 3 more instructions, but:
  MIPS goal: Simpler is Better
Can we implement ≤ in one or more instructions using just slt and the branches?
What about >?
What about ≥?

## Slide 66: Inequalities in MIPS (5/5)
if (g >= h) goto Loop #g:$s0, h:$s1
Loop: . . .
slt $t0,$s0,$s1 # $t0 = 1 if # $s0<$s1 (g<h) beq $t0,$0,Loop # goto Loop # if $t0==0 # if (g  h))
C
M I P S
A slt  beq pair means if(… ≥ …)goto…

## Slide 67: Example: The C Switch Statement (1/3)
Choose among four alternatives depending on whether k has the value 0, 1, 2 or 3. Compile this C code: switch (k) { case 0: f=i+j; break; /* k=0 */ case 1: f=g+h; break; /* k=1 */ case 2: f=g–h; break; /* k=2 */ case 3: f=i–j; break; /* k=3 */ }

## Slide 68: Example: The C Switch Statement (2/3)
This is complicated, so simplify.
Rewrite it as a chain of if-else statements, which we already know how to compile:
  if(k==0) f=i+j; else if(k==1) f=g+h; else if(k==2) f=g–h; else if(k==3) f=i–j;
Use this mapping:
  f:$s0, g:$s1, h:$s2, i:$s3, j:$s4, k:$s5

## Slide 69: Example: The C Switch Statement (3/3)
Final compiled MIPS code: bne $s5,$0,L1 # branch k!=0 add $s0,$s3,$s4 #k==0 so f=i+j j Exit # end of case so Exit L1: addi $t0,$s5,-1 # $t0=k-1 bne $t0,$0,L2 # branch k!=1 add $s0,$s1,$s2 #k==1 so f=g+h j Exit # end of case so Exit L2: addi $t0,$s5,-2 # $t0=k-2 bne $t0,$0,L3 # branch k!=2 sub $s0,$s1,$s2 #k==2 so f=g-h j Exit # end of case so Exit L3: addi $t0,$s5,-3 # $t0=k-3 bne $t0,$0,Exit # branch k!=3 sub $s0,$s3,$s4 #k==3 so f=i-j Exit:

## Slide 70: MIPS Control Instructions Syntax
Instruction Meaning bne $s4,$s5,L Next instr. is at Label if $s4 ≠ $s5 beq $s4,$s5,L Next instr. is at Label if $s4 = $s5 j Label Next instr. is at Label slt $s1,$s2,$s3 if ($s2<$s3) $s1=1; else $s1=0
Formats:
op rs rt rd shamt funct
op rs rt 16 bit address
op 26 bit address
R
I
J

## Slide 71: MIPS Logical Operations
Three basic logical operators in MIPS:
  AND: outputs 1 only if both inputs are 1
  OR: outputs 1 if at least one input is 1
  NOR: outputs 1 if both inputs are 0
Truth Table: standard table listing all possible combinations of inputs and resultant output for each. E.g.,
A | B | A AND B | A OR B | A NOR B
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 72: Logical Instruction Syntax
R-Format
op rs rt rd shamt funct
I-Format
op rs rt 16 bit number
  $s1 = $s2&$s3: and $s1, $s2, $s3
  $s1 = $s2|$3: or $s1, $s2, $s3
  $s1 = ~($s2|$s3): nor $s1, $s2, $s3
There is another important logical function, NOT.
NOT (1) = 0 and NOT (0) = 1.
How to implement NOT function (~) with MIPS instruction?

## Slide 73: Exercise: Implement NOT function with NOR instruction
A NOR 0 = NOT (A)
Nor $s1, $s2, $zero : $s1=~$s2

## Slide 74: A MIPS Computer Architecture

## Slide 75: MIPS Memory Allocation
MIPS Machine Program
Variables declared
once per program
heap: Explicitly created
space, e.g., malloc
Space for saved procedure information